## Slide 1
Hybrid Methods To Downscale Swells To Coral Reef-Lined Coasts
Alba Ricondo,
Laura Cagigal, Nicolás Ripoll, Ana Rueda and
Fernándo J. Méndez
Geomatics and Ocean Engineering Group. Universidad de Cantabria, Santander, Spain
alba.ricondo@unican.es
UNIVERSIDAD DE CANTABRIA
Ge cean
Image from www.freepik.es

## Slide 2
Introduction: Coral Reefs
Kwajalein coral reef, Source: USGS
Coral reefs provide a natural barrier to protect coastal cities, communities and beaches from storm surges and waves
Low-lying atolls (< 3m altitude) frequently exposed to wave-driven inundation events
Coastal hazards are expected to increase in the future with predicted climate change
Inundation event in Roinamur, Source: USGS
1/17

## Slide 3
Motivation
Classical Dynamical Downscaling
Huge amount of data
Accurate but computationally expensive
Hybrid Methods
Inundation forecast
Reduce significantly the amount of data
Fast and efficient
Statistical + Dynamical Tools
Early Warning Systems
2/17

## Slide 4
MDA
Maximum Dissimilarity Algorithm
Dynamical Modelling
SWAN - SWASH
RBF
Radial Basis Functions
subset
dataset
Selection
Propagation
Interpolation
Wave-driven inundation metamodels
3/17

## Slide 5
Wind-Wave conditions
Sea: , ,
Swells:
Tide
, ,
Overtopping volumes
Offshore
Nearshore
Flooding
HyWaves
HySwash
Wind-Wave conditions
+
Wave-driven inundation metamodels
4/17

## Slide 6
Offshore wave dataset
Swells
Sea
, ,
MDA
RBF
SWAN
AGGREGATION
SPECTRAL PARTITIONING
VALIDATION
RBF
SWAN
MDA
HyWaves: Methodology
(Holthuijsen, 2007)
5/17

## Slide 7
St. 2915
Majuro
Arno
St. 2913
St. 2856
St. 2914
St. 2857
St. 2858
St. 2915
St. 2914
St. 2913
St. 2856
St. 2857
St. 2858
Global wave hindcast stations
Wavespectra Library
developed by MetOcean Solutions
Watershed Method
(Hanson and Philips, 2001)
3. Parameterization of sea-swells systems
1. “Super-point”
2. Spectral Partitioning
HyWaves
Sea
, ,
Swells
6/17

## Slide 8
4. MDA
Maximum Dissimilarity Algorithm
5. SWAN
Dynamical Downscaling
HyWaves
Simulating WAves Nearshore (TUDelft)
7/17
500 seas + 500 swells (Camus et al., 2011)

## Slide 9
Interpolation Algorithm
(Rippa 1999)
6. RBF
Radial Basis Functions
“a weighted sum of radial basis functions”
The historical wave climate can be reconstructed at any location in the domain
HyWaves
Based on the 500 + 500 MDA
simulated cases
(Camus et al., 2011)
8/17

## Slide 10
Majuro Atoll
Kwajalein Atoll
Roinamur
Kwajalein
HyWaves: Validation Sites
9/17

## Slide 11
F
E
D
C
B
A
HyWaves: Spectral Wave Climate
Majuro Atoll
Kwajalein Atoll
10/17
Northwest Swells
Southwest Swells
Eastern Swells
% Energy Flux Contribution
% Energy Flux Contribution
Sea
Swell 1
Swell 2
O
A
C
D
F
E
O
B
G
A
C
D
F
E
O
B
Notes: Energy flux contribution
Seasonality
Interannual variability
ENSO events

## Slide 12
Wind-Wave conditions
Sea: , ,
Swells:
Tide
, ,
Overtopping volumes
Offshore
Nearshore
Flooding
HyWaves
HySwash
Wind-Wave conditions
+
Wave-driven inundation metamodels
11/17

## Slide 13
HyWaves
Offshore wave dataset
(historical / emulated)
Nearshore wave dataset
reconstructed at the beginning of the profile
TIME-SERIES
FLOODING VARIABLES
MDA
RBF
SWASH
HySwash: Methodology
Reef bathymetry and coastal topography
Forcings
Wind-Waves-Tide
Flooding model
Inundation maps
12/17
EWS

## Slide 14
HySwash
1. Profiles definition
Kwajalein Atoll
2D domain
two dimensional hydrodynamic models
1D profiles
Assuming constant forcing along width wi
13/17
500 cases / profile
2. MDA
Notes: However, 2D effects on the wave propagation on the reef are not included, which might produce inaccurate results due resonance phenomena for example (this aspect might need to be further analyzed).

## Slide 15
Wave-driven coastal inundation: Metamodels
HySwash
Modelling water levels along the reef
SWASH
Simulating WAves till SHore (TUDelft)
2. Dynamical Donwscaling
Output / profile
Wave-runup
Overtopping rates
14/17
Reef bathymetry and coastal topography
Notes: The variables used to describe the inundation

## Slide 16
3. RBF Interpolation
Historical reconstruction of runup and overtopping rate series
HySwash
15/17

## Slide 17
Wave-driven coastal inundation: Metamodels
Coastal flooding
Hindcast TWL timeseries
Forecast TWL timeseries
Synthetic time series of waves and water level conditions
Historical, present and future climates
Climate change scenarios
Zornoza-Aguado et al.
Flood Inundation Model
LisFlood-FP (University of Bristol)
2D hydrodynamic model
Kwajalein flooding inundation extents
16/17

## Slide 18
Conclusions
2 Nested hybrid models are presented to downscale wave climate from deep waters to the beach crest of coral-reef shorelines
HyWaves methodology has been positively validated with in-situ wave measurements while HySwash methodology still needs validation
Metamodels provide efficient and faster tools when limited by computational resources
17/17

## Slide 19
Thank you very much for your attention
Alba Ricondo
alba.ricondo@unican.es
UNIVERSIDAD DE CANTABRIA
Ge cean
Ocean after the hurricane in Bonaire, Caribbean (www.freepik.com)
Acknowledgements
This work is funded by the Spanish Ministry of Science and Innovation, National Project “Beach4Cast” (PID2019-107053RB-I00).
Notes: <a href='https://www.freepik.com/photos/food'>Food photo created by wirestock - www.freepik.com</a>