## Slide 1
Hybrid flooding system under varying morphodynamic beach states
Manuel Zornoza-Aguado, Beatriz Pérez-Díaz, Sonia Castanedo, Laura Cagigal, Fernando J. Méndez, Javier Sánchez-Espeso, Ignacio García-Utrilla
Geomatics and Ocean Engineering Group, University of Cantabria

## Slide 2
Introduction
Early Warning Systems (EWS): communication systems that help communities prepare for hazardous climate-related events.
    Computationally expensive : executions in near real time
    Need to be fast  libraries of pre-run cases
HYBRID SYSTEMS
Numerical models (dynamical downscaling) + mathematical tools (statistical downscaling)
2014 Storm in Cantabrian Sea

## Slide 3
Introduction
EWS based on pre-run cases
Hybrid approach:
N Cases
Representative topobathymetry
…
Numerical simulations
{Hs1, Tp1, θ1, σ1, η1}
{Hs2, Tp2, θ2, σ2, η2}
{Hs3, Tp3, θ3, σ3, η3}
…
N Flood Maps
Main constraints:
Morphodynamics not taken into account (topobathymetry remains the same)
Local phenomena (resonance, seiches) conditioned to one morphology
Selection algorithms
Radial Basis Functions (RBF)

## Slide 4
Introduction
…
N Cases
MxN Flood Maps
M topobathymetries
EWS based on pre-run cases
Hybrid approach with updated bathymetry:
Numerical simulations
PCA + RBF
…
{Hs1, Tp1, θ1, σ1, η1}
{Hs2, Tp2, θ2, σ2, η2}
{Hs3, Tp3, θ3, σ3, η3}
…
Selection algorithms

## Slide 5
Study area
La Salvé Beach (Laredo, Spain)
4250 metres long
Dissipative white-sand urban beach
Sand spit in Santoña bar-built Estuary
Macrotidal & semidiurnal
Nearby geographical elements:
  Laredo Port
  Asón river mouth
  Mt. Buciero
Sentinel Hub
Google Earth
SurfCantabria
Mt. Buciero
Asón river mouth
Santoña Estuary
Laredo Port
La Salvé Beach
Mean climate
Hs = 1.5 m
Tp = 10 s
θ = 315º
TR = 4.5 m
D50 = 0.23 mm

## Slide 6
Field data
14 UAV-derived topographies + shallow waters (University of Cantabria)
Δx = 0.20m
10 Fieldwork-derived topobathymetries (CEDEX and Nautic Chart)
Δx = 5m
DJI Phantom 4 Pro-V2
RGB camera 20 Mp / 4K
GPS/GLONASS with PPK system

## Slide 7
Open data
GEE images + tide levels
Beach-face slopes
CSIRO hindcast
Calibrated (1)
Validated (2)
(1) Satellite data
IMOS
(2) Buoy data
Puertos del Estado
HyWaves (Ricondo et al, sub.)
CoastSat.slope (Vos et al, 2020)

## Slide 8
Methodology
Offshore waves
Tide levels
Calibration
Validation
Cases selection (MDA)
Waves propagation (SWAN)
Waves reconstruction (RBF)
Synthetic cases (LHS + MDA)
XBeach
PCA + RBF
2D WL maps
Lisflood-FP
Flood extents
HyWaves (Ricondo et al, sub.)
Topobathymetries
Satellite images
Beach slopes
Analogue topobathy
Operational
Analogue forcings
(*)
(*) CoastSat.slope (Vos et al, 2020)

## Slide 9
Methodology
CSIRO hindcast
Sentinel Hub
HyWaves (Ricondo et al., sub.)
XBeach
MDA + SWAN + RBF
Calibrated & Validated
LHS + MDA
Lisflood-FP
PCA + RBF
Hs, Tp, θ, σ, WL
Calibration
Satellite data (IMOS)
Validation
Buoy data (Ports of Spain)
HyWaves
Selection: MDA
Propagation: SWAN
Reconstruction: RBF
XBeach
Non-regular mesh
Surf-beat mode
Warm-up: 1h
Lisflood-FP
Δx = 5 m
Full SWE
Input: Water Level
Albuquerque et al, 2018

## Slide 10
Methodology
Generation of synthetic cases
Latin Hypercube Sampling (LHS)
Selection of cases
Maximum Dissimilarty Algorithm (MDA)
Numerical simulation
XBeach
XBeach simulations set-up
Surf-beat mode
Non-regular rectangular mesh
Δx = 5 m in Laredo Bay
Warm-up: 1h
{Hs, Tp, θ, σ, η}
Principal Components Analysis (PCA)
Series reconstruction
Radial Basis Functions (RBF)
Time series of 2D water level maps

## Slide 11
Results
Forcing:
Hs = 4 m
Tp = 15 s
θ = 300º
WL = 0 m
Forcing:
Hs = 4 m
Tp = 15 s
θ = 300º
WL = 0 m

## Slide 12
Results
Forcing:
Hs = 4 m
Tp = 15 s
θ = 300º
WL = 0 m
Forcing:
Hs = 4 m
Tp = 15 s
θ = 300º
WL = 0 m

## Slide 13
Results

## Slide 14
Results
Validation: March 2014 Event
Hs = 11.7 m
Tp = 18.9 s
θ = 298.4º
WL = 2.4 m
(spring tides)
Javier G. Fraile
EA2CPG

## Slide 15
Results
Water Depth (m)
Hs = 11.7 m
Tp = 18.9 s
θ = 298.4º
WL = 2.4 m
Parking lot

## Slide 16
Conclusions
Hybrid systems with changing topobathymetries allow fast and precise flooding forecasts, suitable for state-of-the-art EWS. Besides a forecast system, reconstructions can be performed with this methodology.
The modelization of river flow and potential port resonances could result in more precise and realistic simulations.
In complex morphologies where resonances can be generated, having two-dimensional water level maps allows us to identify longitudinal seiches. Moreover, the use of varying topobathys allows the identification of additional resonances.
Water level statistics () obtained with XBeach enable the determination of the IG wave level component. This, along with AT, SS and wave set-up serves as input for Lisflood-FP inundation model.

## Slide 17
manuel.zornoza@unican.es
geoocean.unican.es
Manuel Zornoza Aguado
Acknowledgements
This work is funded by the Spanish Ministry of Science and Innovation, National Project “Beach4Cast” (PID2019-107053RB-I00).
Topo-bathymetry and sediment data provided by Centro de Estudios y Experimentación de Obras Públicas (CEDEX).

## Slide 18
HyFlood
η
Boundary Condition for Lisflood-FP:
from Xbeach  ( , )
: std of IG wave
T
Each hour:
+
During an event:
Parameters for Lisflood-FP: